## Slide 1
Hardware-Algorithm Co-Design for Hyperdimensional Computing Based on Memristive System-on-Chip
Yi Huang, Alireza Jaberi Rad, Qiangfei Xia (qxia@umass.edu)
Department of Electrical and Computer Engineering, University of Massachusetts Amherst
0
1
1
1
0
…
1
1
0
0
0
…
0
1
0
1
1
…
Mapping
Classification results
Processing
Classifier
Transformation
Encoding
Encoded HVs
computing
calculul
obliczenia
informatica
…
Text Input
0.072
0.016
0.072
0.016
0.072
Memristive SoC
Hardware aware processing
Core
Core
HVs
Encoded
HVs
0.01
0.13
0
0.03
0.16
…
Classifier
Encoding
Core
Core
Core
Core
…
CPU
Memory
Interconnect
DAC
ADC
Control
Core 9
Core 10
…
Memristive SoC
AI Models
Edge Devices
Results
Data
Challenges and Motivations
Memristive SoC
10 memristive analog computing cores
RSIC-V CPU
On-chip interconnections between CPU, memory and computing Cores
SPI for off-chip communications
Hardware-aware Encoding
Input vectors: Voltage vectors as feature vectors
Random matrix: Conductance matrix using the intrinsic randomness of memristors
Output HVs: Single-step VMM outputs
Simulation and Experimental Results for Language Classification
Memristive computing core
248 × 256 1T1R crossbar array for analog VMM
On-chip TIA, ADC, DAC for A/D conversion
Max Pooling on-chip activation function
HW-Algorithm Co-Design: HDC with VMM
Hardware Platform: Memristive SoC1
Hardware Implementation of HDC with Memristive SoC
Algorithm:
Artificial intelligence (AI) models are too large for edge devices
Most AI models require multiple layers of computation (like DNNs)
Hardware:
Limited computing resources on edge devices
Limited power source on most edge devices
Algorithm solution:
 Brain-inspired hyper-dimensional computing (HDC)
Hardware solution:
 In-memory computing (IMC) hardware based on memristor devices
Hardware-Algorithm co-design solution:
 VMM-based encoding + Single-layer perceptron classifier
SoC: system on chip
CPU: central processing unit
SPI: Serial peripheral interface
1T1R: 1-transistor-1-memristor
TIA: transimpedance amplifier
ADC: analog-to-digital converter
DAC: digital-to-analog converter
Conventional approach
Proposed approach
Memristive Single-layer Perceptron as Classifier
Input data: Encoded HVs after hardware-aware processing in on-chip CPU
Weight matrix: Offline trained conductance matrix
Classification results: Maximum output of analog VMM
HDC requires only 2 layers of computation (while most AI models require multiple layers)
Much lower HV dimensions (512) than conventional HDC (10000)
94.8% savings in hardware utilization resulting in lower energy consumption and less area
SW/SW: Simulation accuracy comparable to existing work2
SW/HW vs SW/SW: Low accuracy degradation shows the memristive single-layer perceptron classifier is robust against hardware non-idealities
HW/SW vs SW/SW: Encoding process is more sensitive than the classifier to hardware non-idealities
HW/HW vs SW/SW: 6% accuracy degradation because of hardware non-idealities
1. TetraMem. Tetramem mx100 soc. https://www.tetramem.com/products, 2024. Accessed: September 11, 2024.
2. Abbas Rahimi, Pentti Kanerva, and Jan M. Rabaey. ”A robust and energy-efficient classifier using brain-inspired hyperdimensional computing.” In Proceedings of the International Symposium on Low Power Electronics and Design, pages 64–69. IEEE., 8 2016..
81256
1T1R Array
Mapping
Encoding
Classifier
Convert to binary feature vectors
Text, Image, Audio, etc.
Binary Vectors
Single-step VMM
Class 1
Class 2
Class 3
Class N
Encoded HV
Class HV
Projected HV
Similarity Check
Encoded HVs
Encoded HVs
Single-layer Perceptron
…
…
Class 1
Class 2
Class 3
Class
N
…
…
Input
Combinational logic operations
Classification Result
Classification Result
HVs: hyperdimensional vectors
VMM: vector-matrix multiplication
HW: hardware
conventional method
HDC with VMM
24821
1T1R Array
SW: software
HW: hardware
SW/SW: software VMM encoding + software single-layer perceptron classifier
Chart: Accuracy(%)
| SW/SW | SW/HW | HW/SW | HW/HW
 | 96.7143 | 96.0714 | 91.9873 | 90.7111
Chart: Accuracy(%)
| Bulgarian | Czech | Danish | German | Greek | English | Estonian | Finnish | French | Hungarian | Italian | Latvian | Lithuanian | Dutch | Polish | Portuguese | Romanian | Slovak | Slovenian | Spanish | Swedish
 | 88.8 | 84.6 | 93.3 | 94.4 | 95.4 | 94.1 | 89 | 92.6 | 91.8 | 93.1 | 94.9 | 87 | 89.7 | 93.5 | 88.5 | 92 | 88.8 | 81.1 | 86.6 | 93.4 | 92.3
88.8
84.6
93.3
94.4
95.4
94.1
89.0
92.6
91.8
93.1
94.9
87.0
89.7
93.5
88.5
92.0
88.8
81.1
86.6
93.4
92.3